## Slide 1
任课教师：王桢
并行硬件和并行软件

## Slide 2: 课程内容
参考资料：
  并行程序设计导论，Peter S Pacheco, 机械工业出版社， 2016
  CHAPTER 2 Parallel Hardware and Parallel Software

## Slide 3: Some background

## Slide 4: Serial hardware and software
input
output
programs
Computer runs one
program at a time.

## Slide 5: The von Neumann Architecture

## Slide 6: Main memory
This is a collection of locations, each of which is capable of storing both instructions and data.
Every location consists of an address, which is used to access the location, and the contents of the location.

## Slide 7: Central processing unit (CPU)
Divided into two parts.
Control unit - responsible for deciding which instruction in a program should be executed. (the boss)
Arithmetic and logic unit (ALU) - responsible for executing the actual instructions. (the worker)
add 2+2

## Slide 8: Key terms
Register – very fast storage, part of the CPU.
Program counter – stores address of the next instruction to be executed.
Bus – wires and hardware that connects the CPU and memory.

## Slide 9
memory
CPU
fetch/read

## Slide 10
memory
CPU
write/store

## Slide 11: von Neumann bottleneck

## Slide 12: An operating system “process”
An instance of a computer program that is being executed.
Components of a process:
  The executable machine language program.
  A block of memory.
  Descriptors of resources the OS has allocated to the process.
  Security information.
  Information about the state of the process.

## Slide 13: Multitasking
Gives the illusion that a single processor system is running multiple programs simultaneously.
Each process takes turns running. (time slice)
After its time is up, it waits until it has a turn again.

## Slide 14: Threading
Threads are contained within processes.
They allow programmers to divide their programs into (more or less) independent tasks.
The hope is that when one thread blocks because it is waiting on a resource, another will have work to do and can run.

## Slide 15: A process and two threads
the “master” thread
starting a thread
Is called forking
terminating a thread
Is called joining

## Slide 16: Modifications to the von neumann model

## Slide 17: Basics of caching
A collection of memory locations that can be accessed in less time than some other memory locations.
A CPU cache is typically located on the same chip, or one that can be accessed much faster than ordinary memory.

## Slide 18: Principle of locality
Accessing one location is followed by an access of a nearby location.
Spatial locality – accessing a nearby location.
Temporal locality – accessing in the near future.

## Slide 19: Principle of locality
float z[1000];
…
sum = 0.0;
for (i = 0; i < 1000; i++)
sum += z[i];

## Slide 20: Levels of Cache
L1
L2
L3
smallest & fastest
largest & slowest

## Slide 21: Cache hit
L1
L2
L3
x sum
y z total
A[ ] radius r1 center
fetch x

## Slide 22: Cache miss
L1
L2
L3
y sum
r1 z total
A[ ] radius center
fetch x
x
main
memory

## Slide 23: Issues with cache
When a CPU writes data to cache, the value in cache may be inconsistent with the value in main memory.
Write-through caches handle this by updating the data in main memory at the time it is written to cache.
Write-back caches mark data in the cache as dirty. When the cache line is replaced by a new cache line from memory, the dirty line is written to memory.

## Slide 24: Cache mappings
Full associative – a new line can be placed at any location in the cache.
Direct mapped – each cache line has a unique location in the cache to which it will be assigned.
n-way set associative – each cache line can be placed in one of n different locations in the cache.

## Slide 25: n-way set associative
When more than one line in memory can be mapped to several different locations in cache
we also need to be able to decide which line should be replaced or evicted.
x

## Slide 26: Example
Table 2.1: Assignments of a 16-line main memory to a 4-line cache

## Slide 27: Caches and programs

## Slide 28: Virtual memory (1)
If we run a very large program or a program that accesses very large data sets, all of the instructions and data may not fit into main memory.
Virtual memory functions as a cache for secondary storage.
Using virtual address

## Slide 29: Virtual memory (2)
It exploits the principle of spatial and temporal locality.
It only keeps the active parts of running programs in main memory.

## Slide 30: Virtual memory (3)
Swap space - those parts that are idle are kept in a block of secondary storage.
Pages – blocks of data and instructions.
  Usually these are relatively large.
  Most systems have a fixed page size that
  currently ranges from 4 to 16 kilobytes.
More details

## Slide 31: Virtual memory (4)
program A
program B
program C
main memory

## Slide 32: Virtual page numbers
When a program is compiled, its pages are assigned virtual page numbers.
When the program is run, a table is created that maps the virtual page numbers to physical addresses.
A page table is used to translate the virtual address into a physical address.
More details

## Slide 33: Page table
Table 2.2: Virtual Address Divided into Virtual Page Number and Byte Offset

## Slide 34: Translation-lookaside buffer (TLB)
Using a page table has the potential to significantly increase each program’s overall run-time.
A special address translation cache in the processor.

## Slide 35: Translation-lookaside buffer (2)
It caches a small number of entries (typically 16–512) from the page table in very fast memory.
Page fault – attempting to access a valid physical address for a page in the page table but the page is only stored on disk.

## Slide 36: Instruction Level Parallelism (ILP)
Attempts to improve processor performance by having multiple processor components or functional units simultaneously executing instructions.

## Slide 37: Instruction Level Parallelism (2)
Pipelining - functional units are arranged in stages.
Multiple issue - multiple instructions can be simultaneously initiated.

## Slide 38: Pipelining

## Slide 39: Pipelining example (1)
Add the floating point numbers 9.87×104 and 6.54×103

## Slide 40: Pipelining example (2)
Assume each stage takes 1 nanosecond (10-9 s).
This for loop takes about 7000 nanoseconds.

## Slide 41: Pipelining (3)
Divide the floating point adder into 7 separate pieces of hardware or functional units.
First unit fetches two operands, second unit compares exponents, etc.
Output of one functional unit is input to the next.

## Slide 42: Pipelining (4)
Table 2.3: Pipelined Addition.
Numbers in the table are subscripts of operands/results.

## Slide 43: Pipelining (5)
One floating point addition still takes 7 nanoseconds.
But 1000 floating point additions now takes 1006 nanoseconds!

## Slide 44: Multiple Issue (1)
Multiple issue processors replicate functional units and try to simultaneously execute different instructions in a program.
adder #1
adder #2
z[1]
z[3]
z[2]
z[4]
for (i = 0; i < 1000; i++)
z[i] = x[i] + y[i];

## Slide 45: Multiple Issue (2)
static multiple issue - functional units are scheduled at compile time.
dynamic multiple issue – functional units are scheduled at run-time.
superscalar

## Slide 46: Speculation (1)
In order to make use of multiple issue, the system must find instructions that can be executed simultaneously.
In speculation, the compiler or the processor makes a guess about an instruction, and then executes the instruction on the basis of the guess.

## Slide 47: Speculation (2)
z = x + y ;
i f ( z > 0)
w = x ;
e l s e
w = y ;
Z will be
positive
If the system speculates incorrectly,
it must go back and recalculate w = y.

## Slide 48: Hardware multithreading (1)
There aren’t always good opportunities for simultaneous execution of different threads.
Hardware multithreading provides a means for systems to continue doing useful work when the task being currently executed has stalled.
  Ex., the current task has to wait for data to be loaded from memory.

## Slide 49: Hardware multithreading (2)
Fine-grained - the processor switches between threads after each instruction, skipping threads that are stalled.
  Pros: potential to avoid wasted machine time due to stalls.
  Cons: a thread that’s ready to execute a long sequence of instructions may have to wait to execute every instruction.

## Slide 50: Hardware multithreading (3)
Coarse-grained - only switches threads that are stalled waiting for a time-consuming operation to complete.
  Pros: switching threads doesn’t need to be nearly instantaneous.
  Cons: the processor can be idled on shorter stalls, and thread switching will also cause delays.

## Slide 51: Hardware multithreading (3)
Simultaneous multithreading (SMT) - a variation on fine-grained multithreading.
Allows multiple threads to make use of the multiple functional units.

## Slide 53: Program, Process, Thread

## Slide 54: Program vs. Process
A program is the code that is stored on your computer that is intended to fulfill a certain task.
There can be multiple instances of a single program, and each instance of that running program is a process.
  Each process has a separate memory address space, which means that a process runs independently and is isolated from other processes.
https://www.backblaze.com/blog/whats-the-diff-programs-processes-and-threads/
Notes: https://www.backblaze.com/blog/whats-the-diff-programs-processes-and-threads/

## Slide 55
Each process has a separate memory address space, which means that a process runs independently and is isolated from other processes. It cannot directly access shared data in other processes.
Switching from one process to another requires some time (relatively) for saving and loading registers, memory maps, and other resources.

## Slide 56: Process vs. Thread
A thread is the unit of execution within a process.
  A process can have 1~n threads.

## Slide 57
Each thread will have its own stack, but all the threads in a process will share the heap.
A problem with one thread in a process will certainly affect other threads and the viability of the process itself.

## Slide 58: Things to review
The program starts out as a text file of programming code,
The program is compiled or interpreted into binary form,
The program is loaded into memory,
The program becomes one or more running processes.
Processes are typically independent of each other,
While threads exist as the subset of a process.
Threads can communicate with each other more easily than processes can
But threads are more vulnerable to problems caused by other threads in the same process.

## Slide 59: Processes vs. Threads — Advantages and Disadvantages

## Slide 60: CPU, Core, Processor

## Slide 61: CPU vs. Core
A core is usually the basic computation unit of the CPU
  it can run a single program context
  or multiple ones if it supports hardware threads such as hyperthreading on Intel CPUs
A CPU may have one or more cores to perform tasks at a given time.
  These tasks are usually software processes and threads that the OS schedules.
  X = number cores * number of hardware threads per core.
Notes: https://superuser.com/questions/1041370/definition-of-a-processor-vs-core-multiprocessor-vs-multicore

## Slide 62: CPU vs. Core
A CPU contains (1-many) cores.
Each core can execute (1-many) threads depending on hyper-threading technology
Notes: https://stackoverflow.com/questions/19225859/difference-between-core-and-processor

## Slide 63: Processor vs. CPU
A processor is a generic term used to describe any sort of CPU, regardless of cores.
A multiprocessor system contains more than one CPU, allowing them to work in parallel.
  This is called SMP, or Symmetric Multi-Processing.
A multicore CPU has multiple cores on one CPU.

## Slide 64
Multi-processor
Multi-Core CPU
Single-core CPU

## Slide 65: Can a single process run in multiple cores?
Yes, a single process can run multiple threads on different cores.
Notes: https://stackoverflow.com/questions/38733670/can-a-single-process-run-in-multiple-cores

## Slide 66: Can a single thread run in multiple cores?
There is no such thing as a single thread running on multiple cores simultaneously.
  Thread migration is possible
It doesn't mean, however, that instructions from one thread cannot be executed in parallel.
There are mechanisms called instruction pipelining and out-of-order execution that allow it.

## Slide 67: Concurrent vs. Parallel

## Slide 68: Concurrent vs. Parallel
A system is said to be concurrent if it can support two or more actions in progress at the same time.
A system is said to be parallel if it can support two or more actions executing simultaneously.
Notes: https://stackoverflow.com/questions/1897993/what-is-the-difference-between-concurrent-programming-and-parallel-programming

## Slide 69
Concurrent = Two queues and one coffee machine.
Parallel = Two queues and two coffee machines.
in progress at the same time.
Executing simultaneously

## Slide 70: Parallel Computing vs. Concurrent Computing
In parallel computing, execution occurs at the same physical instant
  parallel computing is impossible on a (one-core) single processor
concurrent computing consists of process lifetimes overlapping, but execution need not happen at the same instant
  concurrent processes can be executed on one core by interleaving the execution steps of each process via time-sharing slices
https://en.wikipedia.org/wiki/Parallel_computing

## Slide 71
Concurrent Computing
Parallel Computing

## Slide 73
Supplementary materials

## Slide 74
A system that uses physical addressing
Notes: Source: https://csapp.cs.cmu.edu/2e/ch9-preview.pdf

## Slide 75
A system that uses virtual addressing
back
Dedicated hardware on the CPU chip called the memory management unit (MMU) translates virtual addresses on the fly, using a look-up table stored in main memory whose contents are managed by the operating system.

## Slide 76
How a VM system uses main memory as a cache
partitioning the virtual memory into fixed-sized blocks called virtual pages (VPs)
Similarly, physical memory is partitioned into physical pages (PPs) / page frame
Each page is P = 2^p bytes in size

## Slide 77
How a VM system uses main memory as a cache
Unallocated: Pages that have not yet been allocated (or created) by the VM system. Unallocated blocks do not have any data associated with them, and thus do not occupy any space on disk.
Cached: Allocated pages that are currently cached in physical memory
Uncached: Allocated pages that are not cached in physical memory.
back

## Slide 78
Page table
A page table is an array of page table entries (PTEs)
Each PTE consists of a valid bit and an n-bit address field
back