## Slide 1
王桢
wangzh665@mail.sysu.edu.cn
中山大学 计算机学院
国家超级计算广州中心
GPU Programming with CUDA
引言

## Slide 2: 课程主要内容
相关知识背景补充（3-4课时）
  CUDA与GPGPU、C/CPP语言基础
CUDA与并行计算基础（12-16课时）
  GPU架构、CUDA线程、内存结构、通信同步机制、性能优化
  其他并行编程框架（CUDA+MPI，GPGPU与CUDA的关系）
CUDA应用举例（剩余）
  矩阵乘法，排序，图像高斯模糊，Ray Tracing, 等
  CUDA库选择介绍
    Thrust, cuDNN, cuBLAS, 等

## Slide 3: 参考书目（文档）
E. Kandrot and J. Sanders, CUDA by Example: An Introduction to General-Purpose GPU Programming, Pearson, 2010.
  中译版：GPU高性能编程：CUDA实战
N. Wilt, The CUDA Handbook: A Comprehensive Guide to GPU Programming, Prentice Hall, 2013.
  中译版：CUDA专家手册：GPU编程权威指南
J. Cheng, M. Grossman, and T. McKercher, Professional CUDA C Programming, Wrox, 2014.
  中译版：CUDA C编程权威指南
NVIDIA官方文档：
  CUDA C Programming Guide
  CUDA C Programming Best Practice Guide

## Slide 4: 本次课程概要
History of GPU
Why GPU (CUDA)？
GPU (CUDA) 加速效果
安装与项目创建

## Slide 5: History of GPUs … How did they evolve?

## Slide 6: Why Looking at GPU History?
Looking at how things evolved can highlight future directions.
Some of the current architecture decisions won’t make sense without historical perspective.

## Slide 7: Graphic Elements
Vertex: A point with 3D coordinate and color.
Polygons: composed of vertices and edges.
Mesh: A grid of polygons to represent an object.
Objects: Any 2D or 3D entity whose shape could be represented by mesh of arbitrary polygons.
Primitive: Classical geometric shapes can be directly used as primitives (e.g. point, line, cube, cylinder, sphere...) to make parts of objects.
F. Durand, “A Short Introduction to Computer Graphics”, MIT Laboratory for Computer Science
R. Fernando, C. Zeller, “Programming Graphics Hardware Programming Hardware”, NVIDIA.
Notes: A caw modeled as a mesh of triangles.

## Slide 8: Graphic Elements
Texture: An image that is mapped on the surface of polygons on objects to provide a concept of specific material.
Color: The color of each pixel is described by three numbers for intensity of main colors: red, green, and blue, e.g. (255, 0, 255).
Pixel: A computer image is represented by an array of points called pixel with its own color and coordinate (address).
Resolution: The number of pixels in an image determines the resolution of the image, e.g. 320x200, 2560x2048.
Fragment: All necessary data needed to generate a single pixel of final image in output memory, e.g. coordinates, color, depth...
F. Durand, “A Short Introduction to Computer Graphics”, MIT Laboratory for Computer Science
R. Fernando, C. Zeller, “Programming Graphics Hardware Programming Hardware”, NVIDIA.
Notes: A caw modeled as a mesh of triangles.

## Slide 9: Graphic Pipeline
Geometry-Stage:
F. Durand, “A Short Introduction to Computer Graphics”, MIT Laboratory for Computer Science
Several mathematical computation stages to realize 3D virtual scenes into 2D images.
Rasterization(光栅化)-Stage:
Lighting Process
Drawing covered pixels by the primitives (line or triangle) is called rasterization.
lighting properties of all vertices should be found by considering a light source and a viewer at desired point and their angle.
Notes: One of the most important reasons of improving graphic cards was to realize 3D virtual scenes into 2D images. Rendering an image is performed by doing various processes on four basic elements: vertices, primitives, fragments, and pixels. This could be done by passing data through several mathematical computation stages called Graphics Pipeline.
All objects in a 3D scene should be transformed to unique system with their own coordinations. Transformations are done by multiplication with translation, rotation and scaling matrices.
Next, lighting properties of all vertices should be found by considering a light source and a viewer at desired point and their angle.
Drawing covered pixels by the primitives (line or triangle) is called rasterization. Each primitive generates a set of fragments, which all of its properties, including color, texture, depth and visibility, should be calculated in this stage.

## Slide 10: Graphic Pipeline
R. Fernando, C. Zeller, “Programming Graphics Hardware Programming Hardware”, NVIDIA.
Shading-Stage:
Objects should be shaded according to their interaction with light sources.
Notes: Enhancing the scene with multiple light sources and reflections allows for better rendering. So, the objects should be shaded according to their interaction with light sources. As a result, two other stages, vertex shading and pixel shading, were added in 2001. There are various methods of shading.
A shadow ray is considered from the light source to the visible point of the object, if the ray passes the surface then the point is in shadow. In this method, shadow calculations must be performed for all pixels and each light source separately.
the term "vertex shader" is indeed a misnomer. The term "shader" is used for any program that typically runs on the GPU (as opposed to the CPU). The first incarnation of these were pixel shaders, also known as fragment shaders, where the name still made sense.
Then vertex shaders were invented, but they don't actually shade anything; they have the ability to transform a vertex's position in space, and they can pass down per-vertex data to the pixel shader. "Vertex program" would be a better name, but the word "shader" apparently stuck.

## Slide 11: From Numbers to Screen

## Slide 12
Render triangles.
NVIDIA GTX480 can render 1.6 billion triangles per second!

## Slide 13: Before GPUs
Vertices to pixels:
  Transformations done on CPU
  Compute each pixel “by hand”, in series… slow!
Example:
1 million triangles * 100 pixels per triangle *
10 lights * 4 cycles per light computation =
4 billion cycles

## Slide 14
Color Graphic Adapter (CGA 1981)
4 bit RGBI
40 x 25 Characters
320 x 200 Pixel, 16 Colors
640 x 200 Pixel Maximum
16 Kilo Byte Memory
Early GPUs: Early 80s to Late 90s
Notes: RGBI: Red, Green, Blue, Intensity

## Slide 15
Fixed-Function Pipeline
Early GPUs: Early 80s to Late 90s

## Slide 16
Fixed-Function Pipeline
Receives graphics commands and data from CPU
Early GPUs: Early 80s to Late 90s

## Slide 17
Fixed-Function Pipeline
Receives triangle data
Converts them into a form that hardware understands
Store the prepared data in vertex cache
Early GPUs: Early 80s to Late 90s

## Slide 18
Fixed-Function Pipeline
Vertex shading transform and lighting
Assigns per-vertex value (colors, …).
Early GPUs: Early 80s to Late 90s

## Slide 19
Fixed-Function Pipeline
Creates edge equations to interpolate colors across pixels touched by the triangle
Early GPUs: Early 80s to Late 90s

## Slide 20
Fixed-Function Pipeline
Determines which pixel falls into which triangle
For each pixel, interpolate per-pixel values from vertices
Early GPUs: Early 80s to Late 90s

## Slide 21
Fixed-Function Pipeline
Determines the final color of each pixel
Early GPUs: Early 80s to Late 90s

## Slide 22
Fixed-Function Pipeline
The raster operation:
performs color raster operations that blend the color of overlapping objects for transparency and antialiasing
Early GPUs: Early 80s to Late 90s
Notes: antialiasing
[词典]【计】消除混叠现象，消除走样，图形保真
Anti－aliasing （抗锯齿处理）
简单地说主要是应用调色技术将图形边缘的“锯齿”缓和，边缘更平滑。抗锯齿是相对来来说较复杂的技术，一直是高档加速卡的一个主要特征。目前的低档3D加速卡大多不支持反锯齿。

## Slide 23
Fixed-Function Pipeline
The frame buffer interface
manages memory reads/writes.
Early GPUs: Early 80s to Late 90s

## Slide 24: Next Steps
In 2001:
  NVIDIA exposed the application developer to the instruction set of VS/T&L stage
Later:
  General programmability extended to shader stage  trend toward unifying the functionality of different stages as seen by application programmer.
  In graphics pipelines, certain stages do a great deal of floating-points arithmetic on a completely independent data.
    Data independence is exploited  key assumption in GPUs
Notes: "VS/T&L stage" 是指"Vertex Shader/Transformation and Lighting stage"，即顶点着色器/变换与光照阶段。

## Slide 25: The Vision of NVIDIA
"Within the next few years, there will be single-chip graphics devices more powerful and versatile than any graphics system that has ever been built, at any price."
-- David Kirk, NVIDIA, 1998

## Slide 26: In 2006
NVIDIA GeForce 8800 mapped separate graphics stage to a unified array of processors
  For vertex shading, geometry processing, and pixel processing
  Allows dynamic partition

## Slide 27: General Purposed GPU
ref: http://www.nvidia.com/object/tesla_computing_solutions.html
Notes: GPU can achieve 10x performance over CPU.

## Slide 28
L2
FB
SP
SP
L1
TF
Thread Processor
Vtx Thread Issue
Setup / Rstr / ZCull
Geom Thread Issue
Pixel Thread Issue
Input Assembler
Host
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
L2
FB
L2
FB
L2
FB
L2
FB
L2
FB
Exploring the use of GPUs to solve compute intensive problems The birth of GPGPU but there are many constraints
GPUs and associated APIs were designed to process graphics data

## Slide 29: Previous GPGPU Constraints
Input Registers
Fragment Program
Output Registers
Constants
Texture
Temp Registers
per thread per Shader per Context
FB Memory
Dealing with graphics API
  Working with the corner cases of the graphics API
Addressing modes
  Limited texture size/dimension
Shader capabilities
  Limited outputs
Instruction sets
  Lack of Integer & bit ops
Communication limited
No user-defined data types

## Slide 30: The Birth of GPU Computing
Step 1: Designing high-efficiency floating-point and
integer processors.
Step 2: Exploiting data parallelism by having large number of processors
Step 3: Shader processors fully programmable with large instruction cache, instruction memory, and instruction control logic.
Step 4: Reducing the cost of hardware by having multiple shader processors to share their cache and control logic.
Step 5: Adding memory load/store instructions with random byte addressing capability
Step 6: Developing CUDA C/C++ compiler, libraries, and runtime software models.

## Slide 31: Problem With GPUs: Power
Source: http://www.eteknix.com/gigabyte-g1-gaming-geforce-gtx-980-4gb-graphics-card-review/17/

## Slide 32: Problems Faced by GPUs
Need enough parallelism
Under-utilization
Bandwidth to CPU
Still a way to go

## Slide 33: 本次课程概要
History of GPU
Why GPU (CUDA)？
GPU (CUDA)加速效果
安装与项目创建

## Slide 34: Why GPU (CUDA)?
摩尔定律
  英特尔创始人之一戈登·摩尔提出：
  ”集成电路上可容纳的晶体管数目，
  约每隔两年便会增长一倍“
  另一版本为18个月（由英特尔首席执行官大卫·豪斯提出）

## Slide 35: Why GPU (CUDA)?
摩尔定律
Licensed under CC-BY-SA by the author Max Roser.

## Slide 36: Why GPU (CUDA)?
摩尔定律的瓶颈
  晶体管数目≠频率
图片来源：The Economist’s Technology Quartlerly
“The number of people predicting the death of Moore’s Law doubles every two years.”
-Peter Lee, Vice President, Microsoft Research
摩尔定律还能持续多久？
2021/2025年假说
  没有失效
  制程仍在降低
  但有减慢的趋势
量子穿隧效应

## Slide 37: Why GPU (CUDA)?
摩尔定律的瓶颈
  晶体管数目≠频率
图片来源：Ars Technica
摩尔定律还能持续多久？
2021/2025年假说
  没有失效
  制程仍在降低
  但有减慢的趋势
量子穿隧效应
“The number of people predicting the death of Moore’s Law doubles every two years.”
-Peter Lee, Vice President, Microsoft Research

## Slide 38: Why GPU (CUDA)?
串行速度提升已经结束
  无法继续提升频率
  难以继续降低功耗
当前计算机性能提升趋势
  计算机没有变得更快，而是变得更宽
    多核CPU、GPU、超级计算机
  数据级别的并行
    同样的指令作用于多个数据
  线程级别的并行
图片来自网络

## Slide 39: Why GPU (CUDA)?
GPGPU （General Purpose Computing for GPU)
  GPU特征
    高度并行化：同样指令应用于大量数据上
    大量运算核心
图片来自NVIDIA

## Slide 40: Why GPU (CUDA)?
GPGPU
  图形绘制简易流程

## Slide 41: Why GPU (CUDA)?
GPGPU基本思路
  Vertex shader 和 fragment shader 可由用户自行通过shading language编程
  把封装数据封装成图形绘制库所需的数据形式传入
  绘制过程中通过修改shader执行用户编写的程序
    通常是fragment shader
  将结果绘制到texture中传出
  需要很强的图形学编程能力

## Slide 42: Why GPU (CUDA)？
CPU与GPU性能对比
图片来自NVIDIA
Notes: 2011-2012?

## Slide 43: Why GPU (CUDA)？
GPU运算速度发展

## Slide 44: Why GPU (CUDA)?
GPU与超级计算机

## Slide 45: Why GPU (CUDA)?
CUDA vs OpenMP vs MPI
  NVIDIA显卡
  基于GPU线程并行

## Slide 46: Why GPU (CUDA)?
CUDA vs OpenMP vs MPI
  硬件结构
    图中每条波浪线代表一个线程
    每个block包含多个线程
      只有block内部线程能访问其共享内存
    所有线程均可访问全局存储器
图片来自NVIDIA

## Slide 47: Why GPU (CUDA)?
CUDA vs OpenMP vs MPI
  硬件结构
    每个线程由一个CUDA core (a.k.a., streaming processor (SP)) 执行
    Block中的线程以warp形式在streaming multiprocessor (SM)上执行
      每个warp包含32个thread (typically)
      warp中所有thread执行同样的指令 （Single Instruction Multiple Data）
图片来自NVIDIA
Notes: A thread block (or just a block if the context makes it clear) is a collection of threads that run on a single streaming multiprocessor (SM).
A warp is a set of 32 threads within a thread block such that all the threads in a warp execute the same instruction. These threads are selected serially by the SM. Once a thread block is launched on a multiprocessor (SM), all of its warps are resident until their execution finishes.

## Slide 48: Why GPU (CUDA)?
CUDA vs OpenMP vs MPI
  MP: multiprocessing
  跨平台
  基于共享内存的多核系统
    多核个人主机
    超级计算机（截止2017年效率并不好）

## Slide 49: Why GPU (CUDA)?
CUDA vs OpenMP vs MPI
  硬件结构
    每个处理器运行一个线程
    每个处理器有易于访问的片上存储（on-chip memory）
    所有处理器共享全局存储器
图片来自NVIDIA

## Slide 50: Why GPU (CUDA)?
CUDA vs OpenMP vs MPI
  MPI（Message Passing Interface）
    跨平台
    基于信息传递
    常用于计算机集群

## Slide 51: Why GPU (CUDA)?
CUDA vs OpenMP vs MPI
  硬件结构
    多个处理器之间通过网络发送消息交互
图片来自NVIDIA

## Slide 52: Why GPU (CUDA)?
  MPI
    进程相互间可以完全独立
    通信成本高
    价格昂贵
CUDA vs OpenMP vs MPI
  CUDA
    创建线程开销低
    可创建大量线程
    控制流简单
  OpenMP
    创建线程开销高
    线程数目有限
    线程相互间可以完全独立
    控制流复杂

## Slide 53: Why GPU (CUDA)?
CUDA vs OpenCL
  OpenCL: 跨平台的开放标准
生态环境：
  CUDA：用户友好、应用广泛（目前NVIDIA投入更大）
  OpenCL：使用稍显复杂、目前应用范围较窄
支持硬件：
  CUDA：NVIDIA显卡
    硬件针对性更强、效率更高、对学习多核编程更有利
  OpenCL: AMD、NVIDIA、Intel、ARM等硬件
    支持硬件更多、效率因硬件而异、优化因硬件而异
Notes: Open Computing Language

## Slide 54: Why GPU (CUDA)?
CUDA vs OpenCL
  OpenCL: 跨平台的开放标准
生态环境：
  CUDA：用户友好、应用广泛（目前NVIDIA投入更大）
  OpenCL：使用稍显复杂、目前应用范围较窄
支持硬件：
  CUDA：NVIDIA显卡
    硬件针对性更强、效率更高、对学习多核编程更有利
  OpenCL: AMD、NVIDIA、Intel、ARM等硬件
    支持硬件更多、效率因硬件而异、优化因硬件而异
“People who are really serious about software should make their own hardware.”
-图灵奖得主Alan Kay

## Slide 55: 课程概要
History of GPU
Why GPU (CUDA)？
CUDA加速效果
安装与项目创建

## Slide 56: CUDA 加速效果
理论效果 – Amdahl’s Law
  程序效率受限于其可并行的比例
可并行的比例（p）
Chart: 
加速比（s）
Notes: Speedup = T_s / T_p = T_s / (pT_s / #threads + (1-p)T_s), as #threadinfty, Speedup = T_s / (1-p)T_s = 1/ (1-p)

## Slide 57: CUDA 加速效果
理论效果 – Amdahl’s Law
  程序效率受限于其可并行的比例及可供使用的核数
加速比（s）
Chart: 
| 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576 | 2097152 | 4194304 | 8388608 | 16777216 | 33554432 | 67108864 | 134217728 | 268435456 | 536870912 | 1073741824 | 2147483648 | 4294967296 | 8589934592 | 17179869184
P=25% | 1.1429 | 1.2308 | 1.28 | 1.3061 | 1.3196 | 1.3264 | 1.3299 | 1.3316 | 1.3325 | 1.3329 | 1.3331 | 1.3332 | 1.3333 | 1.3333
P=50% | 1.3333 | 1.6 | 1.7778 | 1.8824 | 1.9394 | 1.9692 | 1.9845 | 1.9922 | 1.9961 | 1.998 | 1.999 | 1.9995 | 1.9998 | 1.9999
P=90% | 1.8182 | 3.0769 | 4.7059 | 6.4 | 7.8049 | 8.7671 | 9.3431 | 9.6604 | 9.8273 | 9.9129 | 9.9562 | 9.9781 | 9.989 | 9.9945
P=95% | 1.9048 | 3.4783 | 5.9259 | 9.1429 | 12.549 | 15.4217 | 17.415 | 18.6182 | 19.2844 | 19.6357 | 19.8162 | 19.9077 | 19.9537 | 19.9768
核数（n）

## Slide 58: CUDA 加速效果
案例分析-矩阵乘法
  对C中所有元素，计算
    共有 次向量乘法（内积）
    每次向量乘法为 次浮点数乘法与 次浮点数加法

## Slide 59: CUDA 加速效果
案例分析-矩阵乘法
  策略1：
    创建 个线程，每个计算一个向量内积
    当 大于CUDA计算核心数目时，GPU保持满载

## Slide 60: CUDA 加速效果
案例分析-矩阵乘法
  策略2：
    先创建 个线程计算所有乘法
    再创建 个线程计算所有加法
    更容易保持满载，但创建进程及同步开销也更高

## Slide 61: CUDA 加速效果
CUDA Zone Showcase
Speedup: 45x
Speedup: 44x
Speedup: 48x
Speedup: 90x

## Slide 62: CUDA 加速效果
OpenCV
  跨平台计算机视觉库
图片来自OpenCV.org
Tesla C2050 (448 cores) versus Core i5-760 2.8Ghz

## Slide 63: CUDA 加速效果
TensorFlow
  深度学习
图片来自Laurence Moroney

## Slide 64: CUDA 加速效果
选择你的硬件
  显存，半精度/双精度运算能力
GPU | FP64 | FP16 | Memory
GeForce GTX 1080 Ti | up to 0.355 TFLOPS | less than 0.177 TFLOPS | 11GB
GeForce Titan Xp | up to 0.380 TFLOPS | less than 0.190 TFLOPS | 12GB
GeForce Titan V | up to 6.875 TFLOPS | ~27.5 TFLOPS | 12GB
GeForce RTX 2080 Ti | estimated ~0.44 TFLOPS | 28.5 TFLOPS | 11GB
Titan RTX | estimated ~0.51 TFLOPS | up to 32.6 TFLOPS | 24GB
Tesla K80 | 1.87+ TFLOPS | N/A | 24GB
Tesla P100 | 4.7 ~ 5.3 TFLOPS | 18.7 ~ 21.2 TFLOPS | 12GB or 16GB
Quadro GP100 | 5.2 TFLOPS | 20.7 TFLOPS | 16GB
Tesla V100 | 7 ~ 7.8 TFLOPS | 28 ~31.4 TFLOPS | 16GB or 32GB
Quadro GV100 | 7.4 TFLOPS | 29.6 TFLOPS | 32GB
Quadro RTX 6000 and 8000 | ~ 0.5 TFLOPS | 32.6 TFLOPS | 24/48GB
Tesla T4 | estimated ~0.25 TFLOPS | 16.2 TFLOPS | 16GB

## Slide 65: CUDA 加速效果
选择你的硬件
  性价比
图片来自Phoronix.com
Performance per watt
图片来自Tim Dettmers

## Slide 66: CUDA 加速效果
选择你的硬件
  多GPU并行能力
图片来自LambdaLabs

## Slide 67: 课程概要
History of GPU
Why GPU (CUDA)？
CUDA加速效果
安装与项目创建

## Slide 68: 安装
下载CUDA Toolkit
  下载地址： http://developer.nvidia.com/cuda-downloads
  Toolkit
    nvcc 编译器
    visual profiler
    visual studio integration (windows)
  Samples
    基本功能：device query、band width query等
    线性系统：QR factorization, LU decomposition等
    图算法：最短路径、PageRank等
    模拟：粒子系统、ray tracing等
  显卡驱动

## Slide 69: 安装
安装
  参照说明文档
    https://docs.nvidia.com/cuda/cuda-installation-guide-microsoft-windows/index.html
    https://docs.nvidia.com/cuda/cuda-installation-guide-mac-os-x/index.html
    https://docs.nvidia.com/cuda/cuda-installation-guide-linux/index.html
安装成功后应该能通过
deviceQuery查看支持CUDA的硬件状态

## Slide 70: 创建项目
简单程序
  nvcc直接编译即可
    与gcc/g++类似
CMake
  跨平台自动化建构系统
Notes: there are CUDA APIs for C, C++, Fortran, Python, and Java. We’ll be using CUDA C.
the CUDA C compiler can compile both C and C++ programs, and it can do this because it is a modified C++ compiler.
CUDA is not just a library that can be linked in to an ordinary C program: CUDA requires a special compiler. For example, an ordinary C compiler (such as gcc) generates a machine language executable for a single CPU (e.g., an x86 processor), but the CUDA compiler must generate machine language for two different processors: the host processor and the device processor.

## Slide 71: 创建项目
CMake
  通过CMakeLists.txt 指明源文件、依赖关系、目标文件
    例子：
# 从helloworld.cu构建helloworld项目
# 检查cmake版本及自动寻找CUDA库路径
cmake_minimum_required(VERSION 2.8)
find_package(CUDA QUIET REQUIRED)
# 指明二进制可执行文件名称及源文件名称
cuda_add_executable(
helloworld
src/helloworld.cu)

## Slide 72: 创建项目
CMake
  使用命令行或GUI创建项目文件

## Slide 73: 第一个程序
查询支持CUDA的硬件
  源码
  输出
Device Number: 0
Device name: Tesla C2050
Memory Clock Rate (KHz): 1500000
Memory Bus Width (bits): 384
Peak Memory Bandwidth (GB/s): 144.00
int nDevices;
cudaGetDeviceCount(&nDevices);
for (int i = 0; i < nDevices; i++) {
cudaDeviceProp prop;
cudaGetDeviceProperties(&prop, i);
printf(" Device Number: %d\n", i);
printf(" Device name: %s\n", prop.name);
printf(" Memory Clock Rate (KHz): %d\n", prop.memoryClockRate);
printf(" Memory Bus Width (bits): %d\n", prop.memoryBusWidth);
printf(" Peak Memory Bandwidth (GB/s): %f\n\n",
2.0*prop.memoryClockRate*(prop.memoryBusWidth/8)/1.0e6);
}

## Slide 74
Questions?